## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 6
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 6 :: Topics
Introduction
Assembly Language
Machine Language
Programming
Addressing Modes
Lights, Camera, Action: Compiling, Assembling, & Loading
Odds and Ends

## Slide 3
Jumping up a few levels of abstraction
Architecture: programmer’s view of computer
  Defined by instructions & operand locations
Microarchitecture: how to implement an architecture in hardware (covered in Chapter 7)
Introduction

## Slide 4
Instructions: commands in a computer’s language
  Assembly language: human-readable format of instructions
  Machine language: computer-readable format (1’s and 0’s)
MIPS architecture:
  Developed by John Hennessy and his colleagues at Stanford and in the 1980’s.
  Used in many commercial systems, including Silicon Graphics, Nintendo, and Cisco
Once you’ve learned one architecture, it’s easy to learn others
Assembly Language

## Slide 5
President of Stanford University
Professor of Electrical Engineering and Computer Science at Stanford since 1977
Coinvented the Reduced Instruction Set Computer (RISC) with David Patterson
Developed the MIPS architecture at Stanford in 1984 and cofounded MIPS Computer Systems
As of 2004, over 300 million MIPS microprocessors have been sold
John Hennessy

## Slide 6
Underlying design principles, as articulated by Hennessy and Patterson:
    Simplicity favors regularity
    Make the common case fast
    Smaller is faster
    Good design demands good compromises
Architecture Design Principles

## Slide 7
add: mnemonic indicates operation to perform
b, c: source operands (on which the operation is performed)
a: destination operand (to which the result is written)
C Code
a = b + c;
MIPS assembly code
add a, b, c
Instructions: Addition

## Slide 8
Similar to addition - only mnemonic changes
sub: mnemonic
b, c: source operands
a: destination operand
C Code
a = b - c;
MIPS assembly code
sub a, b, c
Instructions: Subtraction

## Slide 9
Simplicity favors regularity
Consistent instruction format
Same number of operands (two sources and one destination)
easier to encode and handle in hardware
Design Principle 1

## Slide 10
More complex code is handled by multiple MIPS instructions.
C Code
a = b + c - d;
MIPS assembly code
add t, b, c # t = b + c
sub a, t, d # a = t - d
Multiple Instructions

## Slide 11
Make the common case fast
MIPS includes only simple, commonly used instructions
Hardware to decode and execute instructions can be simple, small, and fast
More complex instructions (that are less common) performed using multiple simple instructions
MIPS is a reduced instruction set computer (RISC), with a small number of simple instructions
Other architectures, such as Intel’s x86, are complex instruction set computers (CISC)
Design Principle 2

## Slide 12
Operand location: physical location in computer
  Registers
  Memory
  Constants (also called immediates)
Operands

## Slide 13
MIPS has 32 32-bit registers
Registers are faster than memory
MIPS called “32-bit architecture” because it operates on 32-bit data
Operands: Registers

## Slide 14
Smaller is Faster
MIPS includes only a small number of registers
Design Principle 3

## Slide 15
Name | Register Number | Usage
$0 | 0 | the constant value 0
$at | 1 | assembler temporary
$v0-$v1 | 2-3 | Function return values
$a0-$a3 | 4-7 | Function arguments
$t0-$t7 | 8-15 | temporaries
$s0-$s7 | 16-23 | saved variables
$t8-$t9 | 24-25 | more temporaries
$k0-$k1 | 26-27 | OS temporaries
$gp | 28 | global pointer
$sp | 29 | stack pointer
$fp | 30 | frame pointer
$ra | 31 | Function return address
MIPS Register Set

## Slide 16
Registers:
  $ before name
  Example: $0, “register zero”, “dollar zero”
Registers used for specific purposes:
    $0 always holds the constant value 0.
    the saved registers, $s0-$s7, used to hold variables
    the temporary registers, $t0 - $t9, used to hold intermediate values during a larger computation
    Discuss others later
Operands: Registers

## Slide 17
Revisit add instruction
C Code
a = b + c
MIPS assembly code
# $s0 = a, $s1 = b, $s2 = c
add $s0, $s1, $s2
Instructions with Registers

## Slide 18
Too much data to fit in only 32 registers
Store more data in memory
Memory is large, but slow
Commonly used variables kept in registers
Operands: Memory

## Slide 19
Each 32-bit data word has a unique address
Word-Addressable Memory

## Slide 20
Memory read called load
Mnemonic: load word (lw)
Format:
lw $s0, 5($t1)
Address calculation:
  add base address ($t1) to the offset (5)
  address = ($t1 + 5)
Result:
  $s0 holds the value at address ($t1 + 5)
Any register may be used as base address
Reading Word-Addressable Memory

## Slide 21
Example: read a word of data at memory address 1 into $s3
  address = ($0 + 1) = 1
  $s3 = 0xF2F1AC07 after load
Assembly code
lw $s3, 1($0) # read memory word 1 into $s3
Reading Word-Addressable Memory

## Slide 22
Memory write are called store
Mnemonic: store word (sw)
Writing Word-Addressable Memory

## Slide 23
Example: Write (store) the value in $t4 into memory address 7
  add the base address ($0) to the offset (0x7)
  address: ($0 + 0x7) = 7
  Offset can be written in decimal (default) or hexadecimal
Assembly code
sw $t4, 0x7($0) # write the value in $t4
# to memory word 7
Writing Word-Addressable Memory

## Slide 24
Each data byte has unique address
Load/store words or single bytes: load byte (lb) and store byte (sb)
32-bit word = 4 bytes, so word address increments by 4
Byte-Addressable Memory

## Slide 25
The address of a memory word must now be multiplied by 4. For example,
  the address of memory word 2 is 2 × 4 = 8
  the address of memory word 10 is 10 × 4 = 40 (0x28)
MIPS is byte-addressed, not word-addressed
Reading Byte-Addressable Memory

## Slide 26
Example: Load a word of data at memory address 4 into $s3.
$s3 holds the value 0xF2F1AC07 after load
MIPS assembly code
lw $s3, 4($0) # read word at address 4 into $s3
Reading Byte-Addressable Memory

## Slide 27
Example: stores the value held in $t7 into memory address 0x2C (44)
MIPS assembly code
sw $t7, 44($0) # write $t7 into address 44
Writing Byte-Addressable Memory

## Slide 28
How to number bytes within a word?
Little-endian: byte numbers start at the little (least significant) end
Big-endian: byte numbers start at the big (most significant) end
Word address is the same for big- or little-endian
Big-Endian & Little-Endian Memory

## Slide 29
Jonathan Swift’s Gulliver’s Travels: the Little-Endians broke their eggs on the little end of the egg and the Big-Endians broke their eggs on the big end
It doesn’t really matter which addressing type used – except when the two systems need to share data!
Big-Endian & Little-Endian Memory

## Slide 30
Suppose $t0 initially contains 0x23456789
After following code runs on big-endian system, what value is $s0?
In a little-endian system?
sw $t0, 0($0)
lb $s0, 1($0)
Big-Endian & Little-Endian Example

## Slide 31
Suppose $t0 initially contains 0x23456789
After following code runs on big-endian system, what value is $s0?
In a little-endian system?
sw $t0, 0($0)
lb $s0, 1($0)
Big-endian: 0x00000045
Little-endian: 0x00000067
Big-Endian & Little-Endian Example

## Slide 32
Good design demands good compromises
Multiple instruction formats allow flexibility
  add, sub: use 3 register operands
  lw, sw: use 2 register operands and a constant
Number of instruction formats kept small
  to adhere to design principles 1 and 3 (simplicity favors regularity and smaller is faster).
Design Principle 4

## Slide 33
lw and sw use constants or immediates
immediately available from instruction
16-bit two’s complement number
addi: add immediate
Subtract immediate (subi) necessary?
C Code
a = a + 4;
b = a – 12;
MIPS assembly code
# $s0 = a, $s1 = b
addi $s0, $s0, 4
addi $s1, $s0, -12
Operands: Constants/Immediates

## Slide 34
Binary representation of instructions
Computers only understand 1’s and 0’s
32-bit instructions
  Simplicity favors regularity: 32-bit data & instructions
3 instruction formats:
  R-Type: register operands
  I-Type: immediate operand
  J-Type: for jumping (discuss later)
Machine Language

## Slide 35
Register-type
3 register operands:
  rs, rt: source registers
  rd: destination register
Other fields:
  op: the operation code or opcode (0 for R-type instructions)
  funct: the function
  with opcode, tells computer what operation to perform
  shamt: the shift amount for shift instructions, otherwise it’s 0
R-Type

## Slide 36
Note the order of registers in the assembly code:
add rd, rs, rt
R-Type Examples

## Slide 37
Immediate-type
3 operands:
  rs, rt: register operands
  imm: 16-bit two’s complement immediate
Other fields:
  op: the opcode
  Simplicity favors regularity: all instructions have opcode
  Operation is completely determined by opcode
I-Type

## Slide 38
Note the differing order of registers in assembly and machine codes:
addi rt, rs, imm
lw rt, imm(rs)
sw rt, imm(rs)
I-Type Examples

## Slide 39
Jump-type
26-bit address operand (addr)
Used for jump instructions (j)
Machine Language: J-Type

## Slide 40
Review: Instruction Formats

## Slide 41
32-bit instructions & data stored in memory
Sequence of instructions: only difference between two applications
To run a new program:
  No rewiring required
  Simply store new program in memory
Program Execution:
  Processor fetches (reads) instructions from memory in sequence
  Processor performs the specified operation
Power of the Stored Program

## Slide 42
The Stored Program
Program Counter (PC): keeps track of current instruction

## Slide 43
Start with opcode: tells how to parse rest
If opcode all 0’s
  R-type instruction
  Function bits tell operation
Otherwise
  opcode tells operation
Interpreting Machine Code