## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 6
David Money Harris and Sarah L. Harris

## Slide 2
How do we address the operands?
Register Only
Immediate
Base Addressing
PC-Relative
Pseudo Direct
Addressing Modes

## Slide 3
Register Only
Operands found in registers
  Example: add $s0, $t2, $t3
  Example: sub $t8, $s1, $0
Immediate
16-bit immediate used as an operand
  Example: addi $s4, $t5, -73
  Example: ori $t3, $t7, 0xFF
Addressing Modes

## Slide 4
Base Addressing
Address of operand is:
  base address + sign-extended immediate
  Example: lw $s4, 72($0)
    address = $0 + 72
  Example: sw $t2, -25($t1)
    address = $t1 - 25
Addressing Modes

## Slide 5
PC-Relative Addressing
0x10 beq $t0, $0, else
0x14 addi $v0, $0, 1
0x18 addi $sp, $sp, i
0x1C jr $ra
0x20 else: addi $a0, $a0, -1
0x24 jal factorial
Addressing Modes

## Slide 6
Pseudo-direct Addressing
0x0040005C jal sum
...
0x004000A0 sum: add $v0, $a0, $a1
Addressing Modes

## Slide 7
How to Compile & Run a Program

## Slide 8
Graduated from Yale University with a Ph.D. in mathematics
Developed first compiler
Helped develop the COBOL programming language
Highly awarded naval officer
Received World War II Victory Medal and National Defense Service Medal, among others
Grace Hopper, 1906-1992

## Slide 9
Instructions (also called text)
Data
  Global/static: allocated before program begins
  Dynamic: allocated within program
How big is memory?
  At most 232 = 4 gigabytes (4 GB)
  From address 0x00000000 to 0xFFFFFFFF
What is Stored in Memory?

## Slide 10
MIPS Memory Map

## Slide 11
int f, g, y; // global variables
int main(void)
{
f = 2;
g = 3;
y = sum(f, g);
return y;
}
int sum(int a, int b) {
return (a + b);
}
Example Program: C Code

## Slide 12
int f, g, y; // global
int main(void)
{
f = 2;
g = 3;
y = sum(f, g);
return y;
}
int sum(int a, int b) {
return (a + b);
}
.data
f:
g:
y:
.text
main:
addi $sp, $sp, -4 # stack frame
sw $ra, 0($sp) # store $ra
addi $a0, $0, 2 # $a0 = 2
sw $a0, f # f = 2
addi $a1, $0, 3 # $a1 = 3
sw $a1, g # g = 3
jal sum # call sum
sw $v0, y # y = sum()
lw $ra, 0($sp) # restore $ra
addi $sp, $sp, 4 # restore $sp
jr $ra # return to OS
sum:
add $v0, $a0, $a1 # $v0 = a + b
jr $ra # return
Example Program: MIPS Assembly

## Slide 13
Symbol | Address
Example Program: Symbol Table

## Slide 14
Symbol | Address
f | 0x10000000
g | 0x10000004
y | 0x10000008
main | 0x00400000
sum | 0x0040002C
Example Program: Symbol Table

## Slide 15
Example Program: Executable

## Slide 16
Example Program: In Memory

## Slide 17
Pseudoinstructions
Exceptions
Signed and unsigned instructions
Floating-point instructions
Odds & Ends

## Slide 18
Pseudoinstruction | MIPS Instructions
li $s0, 0x1234AA77 | lui $s0, 0x1234 ori $s0, 0xAA77
clear $t0 | add $t0, $0, $0
move $s1, $s2 | add $s2, $s1, $0
nop | sll $0, $0, 0
Pseudoinstructions

## Slide 19
Unscheduled function call to exception handler
Caused by:
  Hardware, also called an interrupt, e.g., keyboard
  Software, also called traps, e.g., undefined instruction
When exception occurs, the processor:
  Records the cause of the exception
  Jumps to exception handler (at instruction address 0x80000180)
  Returns to program
Exceptions

## Slide 20
Not part of register file
  Cause: Records cause of exception
  EPC (Exception PC): Records PC where exception occurred
EPC and Cause: part of Coprocessor 0
Move from Coprocessor 0
  mfc0 $t0, EPC
  Moves contents of EPC into $t0
Exception Registers

## Slide 21
Exception | Cause
Hardware Interrupt | 0x00000000
System Call | 0x00000020
Breakpoint / Divide by 0 | 0x00000024
Undefined Instruction | 0x00000028
Arithmetic Overflow | 0x00000030
Exception Causes

## Slide 22
Processor saves cause and exception PC in Cause and EPC
Processor jumps to exception handler (0x80000180)
Exception handler:
  Saves registers on stack
  Reads Cause register
  mfc0 $t0, Cause
  Handles exception
  Restores registers
  Returns to program
    mfc0 $k0, EPC
    jr $k0
Exception Flow

## Slide 23
Addition and subtraction
Multiplication and division
Set less than
Signed & Unsigned Instructions

## Slide 24
Signed: add, addi, sub
  Same operation as unsigned versions
  But processor takes exception on overflow
Unsigned: addu, addiu, subu
  Doesn’t take exception on overflow
  Note: addiu sign-extends the immediate
Addition & Subtraction

## Slide 25
Signed: mult, div
Unsigned: multu, divu
Multiplication & Division

## Slide 26
Signed: slt, slti
Unsigned: sltu, sltiu
Note: sltiu sign-extends the immediate before comparing it to the register
Set Less Than

## Slide 27
Signed:
  Sign-extends to create 32-bit value to load into register
  Load halfword: lh
  Load byte: lb
Unsigned:
  Zero-extends to create 32-bit value
  Load halfword unsigned: lhu
  Load byte: lbu
Loads

## Slide 28
Floating-point coprocessor (Coprocessor 1)
32 32-bit floating-point registers ($f0-$f31)
Double-precision values held in two floating point registers
  e.g., $f0 and $f1, $f2 and $f3, etc.
  Double-precision floating point registers: $f0, $f2, $f4, etc.
Floating-Point Instructions

## Slide 29
Name | Register Number | Usage
$fv0 - $fv1 | 0, 2 | return values
$ft0 - $ft3 | 4, 6, 8, 10 | temporary variables
$fa0 - $fa1 | 12, 14 | Function arguments
$ft4 - $ft8 | 16, 18 | temporary variables
$fs0 - $fs5 | 20, 22, 24, 26, 28, 30 | saved variables
Floating-Point Instructions

## Slide 30
Opcode = 17 (0100012)
Single-precision:
  cop = 16 (0100002)
  add.s, sub.s, div.s, neg.s, abs.s, etc.
Double-precision:
  cop = 17 (0100012)
  add.d, sub.d, div.d, neg.d, abs.d, etc.
3 register operands:
  fs, ft: source operands
  fd: destination operands
F-Type Instruction Format

## Slide 31
Set/clear condition flag: fpcond
  Equality: c.seq.s, c.seq.d
  Less than: c.lt.s, c.lt.d
  Less than or equal: c.le.s, c.le.d
Conditional branch
  bclf: branches if fpcond is FALSE
  bclt: branches if fpcond is TRUE
Loads and stores
  lwc1: lwc1 $ft1, 42($s1)
  swc1: swc1 $fs2, 17($sp)
Floating-Point Branches

## Slide 32
Microarchitecture – building MIPS processor in hardware
Bring colored pencils
Looking Ahead