## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 7
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 7 :: Topics
Introduction
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor
Exceptions
Advanced Microarchitecture

## Slide 3
Microarchitecture: how to implement an architecture in hardware
Processor:
  Datapath: functional blocks
  Control: control signals
Introduction

## Slide 4
Multiple implementations for a single architecture:
  Single-cycle: Each instruction executes in a single cycle
  Multicycle: Each instruction is broken into series of shorter steps
  Pipelined: Each instruction broken up into series of steps & multiple instructions execute at once
Microarchitecture

## Slide 5
Program execution time
Execution Time = (#instructions)(cycles/instruction)(seconds/cycle)
Definitions:
  CPI: Cycles/instruction
  clock period: seconds/cycle
  IPC: instructions/cycle = IPC
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance
Processor Performance

## Slide 6
Consider subset of MIPS instructions:
  R-type instructions: and, or, add, sub, slt
  Memory instructions: lw, sw
  Branch instructions: beq
MIPS Processor

## Slide 7
Determines everything about a processor:
  PC
  32 registers
  Memory
Architectural State

## Slide 8
MIPS State Elements

## Slide 9
Datapath
Control
Single-Cycle MIPS Processor

## Slide 10
STEP 1: Fetch instruction
Single-Cycle Datapath: lw fetch

## Slide 11
STEP 2: Read source operands from RF
Single-Cycle Datapath: lw Register Read

## Slide 12
STEP 3: Sign-extend the immediate
Single-Cycle Datapath: lw Immediate

## Slide 13
STEP 4: Compute the memory address
Single-Cycle Datapath: lw address

## Slide 14
STEP 5: Read data from memory and write it back to register file
Single-Cycle Datapath: lw Memory Read

## Slide 15
STEP 6: Determine address of next instruction
Single-Cycle Datapath: lw PC Increment

## Slide 16
Write data in rt to memory
Single-Cycle Datapath: sw

## Slide 17
Read from rs and rt
Write ALUResult to register file
Write to rd (instead of rt)
Single-Cycle Datapath: R-Type

## Slide 18
Determine whether values in rs and rt are equal
Calculate branch target address:
BTA = (sign-extended immediate << 2) + (PC+4)
Single-Cycle Datapath: beq

## Slide 19
Single-Cycle Processor

## Slide 20
Single-Cycle Control

## Slide 21
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
Review: ALU

## Slide 22
Review: ALU

## Slide 23
ALUOp1:0 | Meaning
00 | Add
01 | Subtract
10 | Look at Funct
11 | Not Used
ALUOp1:0 | Funct | ALUControl2:0
00 | X | 010 (Add)
X1 | X | 110 (Subtract)
1X | 100000 (add) | 010 (Add)
1X | 100010 (sub) | 110 (Subtract)
1X | 100100 (and) | 000 (And)
1X | 100101 (or) | 001 (Or)
1X | 101010 (slt) | 111 (SLT)
Control Unit: ALU Decoder

## Slide 24
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 |  |  |  |  |  |  | 
lw | 100011 |  |  |  |  |  |  | 
sw | 101011 |  |  |  |  |  |  | 
beq | 000100 |  |  |  |  |  |  | 
Control Unit Main Decoder

## Slide 25
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 0 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
Control Unit: Main Decoder

## Slide 26
Single-Cycle Datapath: or

## Slide 27
No change to datapath
Extended Functionality: addi

## Slide 28
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 |  |  |  |  |  |  | 
Control Unit: addi

## Slide 29
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 | 1 | 0 | 1 | 0 | 0 | 0 | 00
Control Unit: addi

## Slide 30
Extended Functionality: j

## Slide 31
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 |  |  |  |  |  |  |  | 
Control Unit: Main Decoder

## Slide 32
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 | 0 | X | X | X | 0 | X | XX | 1
Control Unit: Main Decoder

## Slide 33
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC
Review: Processor Performance

## Slide 34
TC limited by critical path (lw)
Single-Cycle Performance

## Slide 35
Single-cycle critical path:
Tc = tpcq_PC + tmem + max(tRFread, tsext + tmux) + tALU + tmem + tmux + tRFsetup
Typically, limiting paths are:
  memory, ALU, register file
  Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
Single-Cycle Performance

## Slide 36
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = ?
Single-Cycle Performance Example

## Slide 37
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
= [30 + 2(250) + 150 + 25 + 200 + 20] ps
= 925 ps
Single-Cycle Performance Example

## Slide 38
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC
= (100 × 109)(1)(925 × 10-12 s)
= 92.5 seconds
Single-Cycle Performance Example