## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 7
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 7 :: Topics
Introduction
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor
Exceptions
Advanced Microarchitecture

## Slide 3
Single-cycle:
  + simple
  cycle time limited by longest instruction (lw)
  2 adders/ALUs & 2 memories
Multicycle:
  + higher clock speed
  + simpler instructions run faster
  + reuse expensive hardware on multiple cycles
  - sequencing overhead paid many times
Same design steps: datapath & control
Multicycle MIPS Processor

## Slide 4
Replace Instruction and Data memories with a single unified memory – more realistic
Multicycle State Elements

## Slide 5
STEP 1: Fetch instruction
Multicycle Datapath: Instruction Fetch

## Slide 6
Multicycle Datapath: lw Register Read
STEP 2a: Read source operands from RF

## Slide 7
Multicycle Datapath: lw Immediate
STEP 2b: Sign-extend the immediate

## Slide 8
Multicycle Datapath: lw Address
STEP 3: Compute the memory address

## Slide 9
Multicycle Datapath: lw Memory Read
STEP 4: Read data from memory

## Slide 10
Multicycle Datapath: lw Write Register
STEP 5: Write data back to register file

## Slide 11
Multicycle Datapath: Increment PC
STEP 6: Increment PC

## Slide 12
Write data in rt to memory
Multicycle Datapath: sw

## Slide 13
Read from rs and rt
Write ALUResult to register file
Write to rd (instead of rt)
Multicycle Datapath: R-Type

## Slide 14
rs == rt?
BTA = (sign-extended immediate << 2) + (PC+4)
Multicycle Datapath: beq

## Slide 15
Multicycle Processor

## Slide 16
Multicycle Control

## Slide 17
Main Controller FSM: Fetch

## Slide 18
Main Controller FSM: Fetch

## Slide 19
Main Controller FSM: Decode

## Slide 20
Main Controller FSM: Address

## Slide 21
Main Controller FSM: Address

## Slide 22
Main Controller FSM: lw

## Slide 23
Main Controller FSM: sw

## Slide 24
Main Controller FSM: R-Type

## Slide 25
Main Controller FSM: beq

## Slide 26
Multicycle Controller FSM

## Slide 27
Extended Functionality: addi

## Slide 28
Main Controller FSM: addi

## Slide 29
Extended Functionality: j

## Slide 30
Main Controller FSM: j

## Slide 31
Main Controller FSM: j

## Slide 32
Instructions take different number of cycles:
  3 cycles: beq, j
  4 cycles: R-Type, sw, addi
  5 cycles: lw
CPI is weighted average
SPECINT2000 benchmark:
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type
Average CPI = (0.11 + 0.2)(3) + (0.52 + 0.10)(4) + (0.25)(5) = 4.12
Multicycle Processor Performance

## Slide 33
Multicycle critical path:
Tc = tpcq + tmux + max(tALU + tmux, tmem) + tsetup
Multicycle Processor Performance

## Slide 34
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = ?
Multicycle Performance Example

## Slide 35
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = tpcq_PC + tmux + max(tALU + tmux, tmem) + tsetup
= tpcq_PC + tmux + tmem + tsetup
= [30 + 25 + 250 + 20] ps
= 325 ps
Multicycle Performance Example

## Slide 36
For a program with 100 billion instructions executing on a multicycle MIPS processor
  CPI = 4.12
  Tc = 325 ps
Execution Time =
Chapter 7 :: Topics

## Slide 37
For a program with 100 billion instructions executing on a multicycle MIPS processor
  CPI = 4.12
  Tc = 325 ps
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(325 × 10-12)
= 133.9 seconds
This is slower than the single-cycle processor (92.5 seconds). Why?

## Slide 38
Program with 100 billion instructions
Execution Time = (# instructions) × CPI × Tc
= (100 × 109)(4.12)(325 × 10-12)
= 133.9 seconds
This is slower than the single-cycle processor (92.5 seconds). Why?
Not all steps same length
Sequencing overhead for each step (tpcq + tsetup= 50 ps)
Multicycle Performance Example

## Slide 39
Review: Single-Cycle Processor

## Slide 40
Review: Multicycle Processor