## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 8
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 8 :: Topics
Introduction
Memory System Performance Analysis
Caches
Virtual Memory
Memory-Mapped I/O
Summary

## Slide 3
Computer performance depends on:
  Processor performance
  Memory system performance
Memory Interface
Introduction

## Slide 4
In prior chapters, assumed access memory in 1 clock cycle – but hasn’t been true since the 1980’s
Processor-Memory Gap

## Slide 5
Make memory system appear as fast as processor
Use hierarchy of memories
Ideal memory:
  Fast
  Cheap (inexpensive)
  Large (capacity)
But can only choose two!
Memory System Challenge

## Slide 6
Memory Hierarchy

## Slide 7
Exploit locality to make memory accesses fast
Temporal Locality:
  Locality in time
  If data used recently, likely to use it again soon
  How to exploit: keep recently accessed data in higher levels of memory hierarchy
Spatial Locality:
  Locality in space
  If data used recently, likely to use nearby data soon
  How to exploit: when access data, bring nearby data into higher levels of memory hierarchy too
Locality

## Slide 8
Hit: data found in that level of memory hierarchy
Miss: data not found (must go to next level)
Hit Rate = # hits / # memory accesses
= 1 – Miss Rate
Miss Rate = # misses / # memory accesses
= 1 – Hit Rate
Average memory access time (AMAT): average time for processor to access data
AMAT = tcache + MRcache[tMM + MRMM(tVM)]
Memory Performance

## Slide 9
A program has 2,000 loads and stores
1,250 of these data values in cache
Rest supplied by other levels of memory hierarchy
What are the hit and miss rates for the cache?
Memory Performance Example 1

## Slide 10
A program has 2,000 loads and stores
1,250 of these data values in cache
Rest supplied by other levels of memory hierarchy
What are the hit and miss rates for the cache?
Hit Rate = 1250/2000 = 0.625
Miss Rate = 750/2000 = 0.375 = 1 – Hit Rate
Memory Performance Example 1

## Slide 11
Suppose processor has 2 levels of hierarchy: cache and main memory
tcache = 1 cycle, tMM = 100 cycles
What is the AMAT of the program from Example 1?
Memory Performance Example 2

## Slide 12
Suppose processor has 2 levels of hierarchy: cache and main memory
tcache = 1 cycle, tMM = 100 cycles
What is the AMAT of the program from Example 1?
AMAT = tcache + MRcache(tMM)
= [1 + 0.375(100)] cycles
= 38.5 cycles
Memory Performance Example 2

## Slide 13
Amdahl’s Law: the effort spent increasing the performance of a subsystem is wasted unless the subsystem affects a large percentage of overall performance
Co-founded 3 companies, including one called Amdahl Corporation in 1970
Gene Amdahl, 1922-

## Slide 14
Highest level in memory hierarchy
Fast (typically ~ 1 cycle access time)
Ideally supplies most data to processor
Usually holds most recently accessed data
Cache

## Slide 15
What data is held in the cache?
How is data found?
What data is replaced?
Focus on data loads, but stores follow same principles
Cache Design Questions

## Slide 16
Ideally, cache anticipates needed data and puts it in cache
But impossible to predict future
Use past to predict future – temporal and spatial locality:
  Temporal locality: copy newly accessed data into cache
  Spatial locality: copy neighboring data into cache too
What data is held in the cache?

## Slide 17
Capacity (C):
  number of data bytes in cache
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set
Cache Terminology

## Slide 18
Cache organized into S sets
Each memory address maps to exactly one set
Caches categorized by # of blocks in a set:
  Direct mapped: 1 block per set
  N-way set associative: N blocks per set
  Fully associative: all cache blocks in 1 set
Examine each organization for a cache with:
  Capacity (C = 8 words)
  Block size (b = 1 word)
  So, number of blocks (B = 8)
How is data found?

## Slide 19
C = 8 words (capacity)
b = 1 word (block size)
So, B = 8 (# of blocks)
Ridiculously small, but will illustrate organizations
Example Cache Parameters

## Slide 20
Direct Mapped Cache

## Slide 21
Direct Mapped Cache Hardware

## Slide 22
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?
Direct Mapped Cache Performance

## Slide 23
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 3/15
= 20%
Temporal Locality
Compulsory Misses
Direct Mapped Cache Performance

## Slide 24
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?
Direct Mapped Cache: Conflict

## Slide 25
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 10/10
= 100%
Conflict Misses
Direct Mapped Cache: Conflict

## Slide 26
N-Way Set Associative Cache

## Slide 27
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?
N-Way Set Associative Performance

## Slide 28
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 2/10
= 20%
Associativity reduces
conflict misses
N-Way Set Associative Performance

## Slide 29
Reduces conflict misses
Expensive to build
Fully Associative Cache

## Slide 30
Increase block size:
  Block size, b = 4 words
  C = 8 words
  Direct mapped (1 block per set)
  Number of blocks, B = 2 (C/b = 8/4 = 2)
Spatial Locality?

## Slide 31
Cache with Larger Block Size

## Slide 32
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = ?
Direct Mapped Cache Performance

## Slide 33
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 1/15
= 6.67%
Larger blocks
reduce compulsory misses
through spatial locality
Direct Mapped Cache Performance

## Slide 34
Capacity: C
Block size: b
Number of blocks in cache: B = C/b
Number of blocks in a set: N
Number of sets: S = B/N
Organization | Number of Ways (N) | Number of Sets (S = B/N)
Direct Mapped | 1 | B
N-Way Set Associative | 1 < N < B | B / N
Fully Associative | B | 1
Cache Organization Recap

## Slide 35
Cache is too small to hold all data of interest at once
If cache full: program accesses data X & evicts data Y
Capacity miss when access Y again
How to choose Y to minimize chance of needing it again?
Least recently used (LRU) replacement: the least recently used block in a set evicted
Capacity Misses

## Slide 36
Compulsory: first time data accessed
Capacity: cache too small to hold all data of interest
Conflict: data of interest maps to same location in cache
Miss penalty: time it takes to retrieve a block from lower level of hierarchy
Types of Misses

## Slide 37
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
LRU Replacement

## Slide 38
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
LRU Replacement

## Slide 39
What data is held in the cache?
  Recently used data (temporal locality)
  Nearby data (spatial locality)
How is data found?
  Set is determined by address of data
  Word within block also determined by address
  In associative caches, data could be in one of several ways
What data is replaced?
  Least-recently used way in the set
Cache Summary

## Slide 40
Bigger caches reduce capacity misses
Greater associativity reduces conflict misses
Adapted from Patterson & Hennessy, Computer Architecture: A Quantitative Approach, 2011
Miss Rate Trends

## Slide 41
Bigger blocks reduce compulsory misses
Bigger blocks increase conflict misses
Miss Rate Trends

## Slide 42
Larger caches have lower miss rates, longer access times
Expand memory hierarchy to multiple levels of caches
Level 1: small and fast (e.g. 16 KB, 1 cycle)
Level 2: larger and slower (e.g. 256 KB, 2-6 cycles)
Most modern PCs have L1, L2, and L3 cache
Multilevel Caches

## Slide 43
Intel Pentium III Die